## Slide 1: AI-Based EV Charging Demand Prediction
Load Management | Internship Capstone Prototype

## Slide 2: Problem & Objectives
Simultaneous EV charging can increase peak electricity demand.
Forecast hourly charging energy using historical patterns.
Demonstrate capacity-aware shifting of flexible demand.
Visualize demand, forecasts, and schedule comparison.

## Slide 3: Dataset & Features
2,400 simulated sessions across 180 days; 12 simulated stations.
Session fields: timestamps, duration, charger power, energy, station, temperature, tariff.
Hourly features: hour, weekday, month, weekend, lag-1, lag-24 and rolling demand.
Important: synthetic data are for demonstration, not real-world validation.

## Slide 4: System Architecture
Session data → cleaning → hourly aggregation
Feature engineering → Random Forest regression
Forecast evaluation: MAE, RMSE and R²
Capacity-aware scheduler → Streamlit dashboard

## Slide 5: AI Model & Evaluation
Random Forest Regressor: 160 trees, depth 12.
Chronological split: first 80% train, final 20% test.
Holdout metrics on simulated data: MAE 6.41 kWh; RMSE 10.17 kWh; R² 0.236.
Future work: compare Gradient Boosting and seasonal baselines.

## Slide 6: Load Management
Choose an hourly capacity limit.
Cap excess demand and shift aggregate energy to later hours with spare capacity.
Compare original peak with scheduled peak and report unallocated energy.
Full system must enforce vehicle deadlines, energy needs, and charger limits.

## Slide 7: Dashboard & Demonstration
Demand overview: session count, energy, station count, hourly trend.
Forecast model: actual versus predicted demand.
Load scheduling: capacity slider and before/after profile.
Run with: python src/train_model.py; streamlit run app.py

## Slide 8: Conclusion & Future Scope
Prototype completes the end-to-end forecasting and visualization workflow.
Use real, documented charging-session data for trustworthy evaluation.
Upgrade to vehicle-level optimization with PuLP or OR-Tools.
Add tariff, weather, holidays, charger occupancy and live monitoring.